## Slide 1: Energy Balancing Overview After the Day and Invoicing
This information is a high-level summary of the Energy Balancing Process.
The https://www.gasgovernance.co.uk/UNC is the agreement between the gas transporters and the gas shippers which sets out the detailed rules.
This summary is intended to assist customers to understand the Energy Balancing process, but you must not rely on the contents of this summary and should always refer to the rules as set out in the UNC.
For full details of the terms under which National Gas Transmission PLC is making this summary available please see Terms and Conditions | National Gas

## Slide 2: Context
Energy Balancing is a key aspect of the commercial regime, in which shippers are incentivised to balance their inputs and outputs from the system, which helps to keep the NTS physically balanced.
National Gas (NG) plays a pivotal role in the GB gas market. We own and operate the Gas National Transmission System (NTS), a high-pressure gas network that transports gas throughout England, Scotland and Wales. As owner and System Operator (SO), our primary concern is the safe operation of the NTS.
Gas shippers are incentivised to encourage them to balance inputs and outputs every day – what goes in must equal what comes out. In our role as residual balancer, if we think the system is likely to move outside of the acceptable range of balance, we can carry out a market-balancing action. When we do this, we’re attempting to change the physical flows of gas into or from the system through market trades. This places a greater financial incentive on gas shippers to balance the system themselves.
Xoserve also hold a key industry role as the Central Data Service Provider. The services they provide includes the management of the Gemini system (used to record shipper nominations and allocations), Energy Balancing billing and the Credit and Risk Management process for the Energy Balancing regime.

## Slide 3
After the Day and Invoicing processes simplified
1. After the day
2. Invoice
3. Investigation
4. Adjustment
Xoserve issues shippers with an invoice
National Gas to update Gemini with the shippers' allocations
If any error is identified National Gas will carry out an investigation to determine the correct energy values
If step 3 brings about a change, Xoserve will process an adjustment

## Slide 4: The end-to-end process : explained
1. After the day
Responsibility - National Gas Energy Balancing Team What actually happens - National Gas will receive measurement data from all NTS connected sites and where required NG will update Gemini measurements and shipper allocations before the window for editing data closes.
Timings and detail – The close out dates are defined in UNC and after those dates, no further amendments can be made to Gemini and invoices will be based on the closed out values. If any details require amendment, these should ideally be notified to National Gas ahead of the time shown below to enable processing before close out:
Exit Points D+5 (5 calendar days after the gas day). Notification of amendment by 2.30pm on D+5.
Entry points M+15 (calendar month plus 15 business days). Notification of amendment by 2.30pm on M+15.
Interconnection Points (IPs) follow EU nomination rules (the Gemini nomination is used as the allocation). Close out is D+1. Notification of amendment by 12pm on D+1.
For details see UNC TPD Section E 1.8 Close-out rules / or for Interconnectors EID Section C Nominations & Section D Allocations

## Slide 5: The end-to-end process : explained
Responsibility – Correla on behalf of Xoserve What actually happens = Shippers are invoiced based on Gemini allocation data. Correla issue invoice files via the IX system. These are sent in an industry agreed format as csv files, for example, the Energy Balancing invoice file (BAL) is issued as an .IDB file.
Timings and detail = Energy Balancing Invoicing is carried out on the 23rd business day after the calendar month ends. For example, January usage will be invoiced at the beginning of March). The Amendment invoice is issued on the 18th business day for the previous month (January usage will be invoiced towards the end of February).
A comprehensive list of invoice charges and the latest Billing Calendar are available on the Xoserve Website Invoice Information
2. Invoice

## Slide 6: Who to contact
1. After the day
Summary: Pre & Post Close Out Measurement or Allocation Queries
For Exit Sites email - box.uniquesites@nationalgas.com
For Entry Sites email - box.energybalancing@nationalgas.com
Summary : Pre & Post Close Out EU Nomination Queries
Email - box.NTS.EnergyBalance@nationalgas.com
Summary: Physical Meter Error Queries
Email – box.meterassurance@nationalgas.com
Get in touch via email. We’re also happy to arrange video calls. Just get in touch and we can contact you via Microsoft Teams.
Notes: Summary: Pre & Post Close Out Measurement or Allocation Queries
For Exit Sites email - box.UniqueSites@nationalgas.com
For Entry Sites email - box.EnergyBalancing@nationalgas.com
Summary : Pre & Post Close Out EU Nomination Queries
Email - box.NTS.EnergyBalance@nationalgas.com
Summary: Physical Meter Error Queries
Email – box.meterassurance@nationalgas.com

## Slide 7: Who to contact in Correla
For Invoices:
Energy Balancing Invoices
ebi.billing@xoserve.com
Process Owner Contacts:
Louise Tulk – louise.tulk@correla.com Telephone – 03708 080 303
Sharon Whitehead - Sharon.d.whitehead@correla.com Telephone - 03708 080 263
EBI Team Email Box Account: ebi.billing@xoserve.com
Amendment Invoices
recandrbd.billing@xoserve.com
2. Invoice

## Slide 8: The end-to-end process : explained
Responsibility - National Gas Energy Balancing Team What actually happens - Occasionally there may be circumstances where the allocated quantity in Gemini is incorrect due to a billing, data or metering error. This will cause the incorrect amount to be billed in the original invoice
Depending on the circumstances, a billing adjustment may be required. National Gas will investigate any potential reconciliations and calculate the correct energy which should be allocated to the shipper.
Note that the allocated figure within Gemini is not updated post close out, this process is currently held offline.
Different rules apply to Entry and Exit sites, which are detailed on the following slide
Process - If an issue is identified by National Gas or a Shipper, the National Gas Energy Balancing Team will investigate and keep customers updated. The length of time to investigate will depend on the circumstances and information available. However, customers will be advised as the investigation progresses and notified at the stages shown below:
Acknowledgement & estimation of time to complete
Agreement of revised energy values & expected time to complete & sign off
Sent to Correla for processing
3. Investigation

## Slide 9: The end to end process explained: Reconciliations & Adjustments
For full details please refer to the UNC. The information below is for guidance only.
UNC TPD Section E (Daily Quantities, Imbalances and Reconciliation): Section E defines Reconciliations as applicable only to System Exit Point meter readings (adjusting the corrected reading and the previous reading)
Section S (Invoices & Payment) Section 1.4.4 indicates that no value can be reconciled/adjusted after the Code Cut Off Date. This translates to 3 full financial years (UNC General Terms Section C- Interpretation).
UNC TPD Section S 1.8 – (Invoice Adjustment). This section details the circumstances in which an adjustment can be issued due to an incorrectly stated invoice amount. National Gas will apply the provisions of this section to anything outside UNC Section E, such as NTS Entry Points.
Section S1.8.2 indicates that the cut off period for adjustments is 18 months from the original invoice. This means that National Gas should notify shippers of an incorrect invoice (detailing the invoice number and incorrect allocations) or shippers should query incorrect allocations within 18 months of receiving the original invoice or else the incorrect invoice cannot be amended.
The applicable rules for different site types are listed with the Appendix
3. Investigation
CURRENT FINANCIAL YEAR |  | CAN RECONCILE BACK TO :
From 01/04/23 | Up To 31/03/24 | 01/04/2020
From 01/04/24 | Up To 31/03/25 | 01/04/2021
From 01/04/25 | Up To 31/03/26 | 01/04/2022
From 01/04/26 | Up To 31/03/27 | 01/04/2023
From 01/04/27 | Up To 31/03/28 | 01/04/2024
From 01/04/28 | Up To 31/03/29 | 01/04/2025

## Slide 10: Who to contact
Summary: Reconciliations
Email - box.meterassurance@nationalgas.com
Other useful contacts:
Summary : NTS to LDZ Offtakes & Non NTS connected site Reconciliations & Methodology
Owner - Relevant Distribution Network Operator to the LDZ (Local Distribution Zone)
WWU – Catherine Litster - GasQuality@wwutilities.co.uk
NGN – Luke Warner – LWarner@northerngas.co.uk , Ben Hanley - bhanley@northerngas.co.uk
SGN – Shaun Stephenson - gasquality@sgn.co.uk
Cadent – Simon Howard - metering.me2@cadentgas.com
If you are a customer and believe a reconciliation may be required please see the Reconciliation Checklist in Appendix 1 will information which will be required from Shippers or Asset Owners
3. Investigation

## Slide 11: The end to end process : explained
Trades and Nominations (Including IP Nominations)
If a Trade or Nomination has been identified in error AND there is evidence the fault is with National Gas or its systems (Gemini), raise a ticket with Gemini App Support servicedesk@xoserve.com and email the query to the National Gas Energy Balancing Team.
Contact: box.NTS.EnergyBalance@nationalgas.com
4. Adjustment

## Slide 12: The end to end process : explained
Responsibility - Correla What actually happens - Once notified of the corrected energy values, Correla will calculate the adjusted values and issue corrected charges on the next available invoice. An email is also issued which contains supporting data.
Timings and detail:
Energy Balancing Invoice - Used for adjusting Cashout & Scheduling charges
Adjustments will appear on the Energy Balancing Invoice file (IDB). Within the ‘D17’ record type there is a field which will include a unique reference to the adjustment which can be mapped back to the supporting data issued via email .
Amendments Invoice (AMS) - Used for Commodity Reconciliations
If allocations are changed then there may also be an adjustment to Commodity charges, this would be invoiced via the Amendment Invoice (AMS). AMS allows for a wide range of adjustments including Commodity and LDZ Reconciliations .
Request To Bill (RTB) - This can be used to expedite adjustments in urgent circumstances
The Request To Bill process can be used for adjustments of great urgency and significance to customers. Please contact the National Gas Energy Balancing team for urgent requests
4. Adjustment

## Slide 13: Appendix 1
Charge codes & reconciliation details

## Slide 14: Balancing Invoice Charge Codes
BAL - ENERGY BALANCING INVOICE (Gemini Invoice) |  | 
BOTH | ADS | ADH SMEAR CHARGE
BOTH | B40 | EBI THEFT OF GAS - GAS
BOTH | B43 | EBI INTEREST
BOTH | B44 | ENERGY LATE PAYMENT RECOVERY CHARGE - CR
BOTH | B45 | ENERGY LATE PAYMENT RECOVERY CHARGE - DR
BOTH | B62 | ADH REC GAS CASHOUT DUE TRANSCO
BOTH | B63 | ADH REC GAS CASHOUT DUE SHPPER
BOTH | B71 | ADH DAILY CASHOUT DUE TRANSCO
BOTH | B72 | ADH CUM CASHOUT DUE TRANSCO
BOTH | B73 | ADH FLEX PAYT DUE TRANSCO
BOTH | B74 | ADH ENTRY SCHEDULING CHG
BOTH | B75 | ADH EXIT DMA SCHEDULING CHG
BOTH | B76 | ADH EXIT DMC SCHEDULING CHG
BOTH | B77 | ADH BAL NEUTRALITY SMEAR
BOTH | B78 | ADH NDM RECONCILIATION SMEAR
BOTH | B79 | ADH TOP UP SMEAR
BOTH | B80 | ADH DAILY CASHOUT DUE SHIPPER
BOTH | B81 | ADH CUM CASHOUT DUE SHIPPER
BOTH | B82 | ADH FLEX PAYMENT DUE SHIPPER
BOTH | B83 | UGF EXIT CASHOUT DUE TRANSCO
BOTH | B84 | UGF ENTRY CASHOUT DUE SHIPPER
BOTH | B85 | CSEP CASHOUT DUE TRANSCO
BOTH | B86 | CSEP CASHOUT DUE SHIPPER
BOTH | B87 | ADH DM RECONCILIATION SMEAR
BOTH | B90 | PHYSICAL RENOM INCEN CH ADJ
BOTH | B91 | TRANSCO TRADE BUY GAS COST ADJ
BOTH | B92 | TRANSCO TRADE SELL GAS COST ADJ
BOTH | B93 | INCENTIVISED NOMINATION SCH - ADJ
BOTH | CCS | CUMULATIVE CASHOUTS-DUE SHP'R
BOTH | CCT | CUMULATIVE CASHOUTS-DUE T'SCO
BOTH | CNU | BALANCING NEUTRALITY SMEAR
BOTH | DCS | DAILY CASHOUT (DUE SHIPPER)
BOTH | DCT | DAILY CASHOUT -DUE TRANSCO
BOTH | DMR | DM RECONCILIATION
BOTH | DXS | DMA EXIT SCHEDULING-TR'SCO
BOTH | ESC | ENTRY SCHEDULING-DUE TR'SCO
BOTH | EXS | EXIT SCHEDULING-DUE TR'SCO
BOTH | FPS | FLEXIBILITY PAYMENT-DUE SHP'R
BOTH | FPT | FLEXIBILITY PAYMENT-DUE T'SCO
BOTH | INS | INCENTIVISED NOMINATION SCHEME
BOTH | PRI | PHYSICAL RENOMINATION INCENT
BOTH | REC | NDM/CSEP RECONCILIATION SMEAR
BOTH | TTB | TRANSCO TRADE BUY GAS COST
BOTH | TTS | TRANSCO TRADE SELL GAS COST
BOTH | TUT | TOP UP NEUTRALITY SMEAR
BOTH | DUT | GDE DEEMED TRADE CHARGE
BOTH | B94 | ADJUSTMENT TO GDE DEEMED TRADE CR DR
BOTH | TSS | DSR FUND IMBALANCE CHARGE
BOTH | B95 | ADJUSTMENT TO DSR FUND IMBALANCE CHARGE CR DR
BOTH | DSP | DSR COMPENSATION PAYMENT
BOTH | B96 | ADJUSTMENT TO DSR COMPENSATION PAYMENT CR DR
Note that Transco was formerly the name of National Grid Gas plc, which is now National Gas Transmission PLC
This is an extract from the Xoserve comprehensive list of invoice charges, available online:
Invoice type, charges & VAT (xoserve.com)

## Slide 15: Reconciliation Examples
Scenario: Cashout and scheduling charges need to be adjusted due to an incorrect allocation figure.
The Shipper “ABC” will receive the following supporting information via email which shows the original data and the revised data which has been used for the adjustment.
In this example, Shipper ABC would receive a credit of £567.54 relating to Scheduling Charges and £2,204.61 in relation to Cashout – details are provided within the relevant tabs.
The total of £2,772.15 would be paid to the Shipper ABC via Energy Balancing Invoice file (IDB).
There may also be a change to the Commodity Charges which would be processed via the Amendments (AMS) invoice.
Note: For Storage Customers there is no Commodity charge so AMS invoice does not apply.
Scenario: Cashout needs to be adjusted due to an incorrect trade figure
The revised energy value is shown on the relevant tab and the Shipper ABC would receive payment of £8,169.65 via the Energy Balancing Invoice file (IDB) due to their corrected balance position.
Note: The Energy Balancing Invoice adjustment process will be used in the of error due to National Gas as the Transporter (e.g. system errors or data input error).

## Slide 16: UNC Reconciliation obligation tables
Site Type | Entry/Exit | Close out | Reconciliation rules in place
Terminals | NTS entry point | M+15 | No UNC post closeout measurement reconciliation mechanism – Although invoices can be queried and allocations amended under Section S
Storage Withdrawal | NTS entry point | M+15 | No UNC post closeout measurement reconciliation mechanism – Although invoices can be queried and allocations amended under Section S
Interconnector Import | NTS entry point | D+1 | UNC reconciliation guidelines for measurement & allocation amendments (Code Cut Off Date)
Power Stations | NTS exit point | D+5 | UNC reconciliation guidelines for measurement & allocation amendments (Code Cut Off Date)
Industrials | NTS exit point | D+5 | UNC reconciliation guidelines for measurement & allocation amendments (Code Cut Off Date)
Storage Injection | NTS exit point | D+5 | UNC reconciliation guidelines for measurement & allocation amendments (Code Cut Off Date)
Storage Own Use Gas | NTS exit point | D+5 | UNC reconciliation guidelines for measurement & allocation amendments (Code Cut Off Date)
Interconnector Export | NTS exit point | D+1 | UNC reconciliation guidelines for measurement & allocation amendments (Code Cut Off Date)

## Slide 17: Reconciliation Check List
UNIQUE SITES | INTERCONNECTOR | OFFTAKES | TRADES | TERMINALS | STORAGE (Energy Balance invoice only)
OWNER: |  |  |  |  | 
Gas Energy Management (GEM) /Meter Assurance (MA) (Data) | Balancing Strategy (BS) / Meter Assurance | Distribution Network / Meter Assurance | Balancing Strategy / Meter Assurance | Gas Energy Management /Meter Assurance (Data) | Gas Energy Management /Meter Assurance (Data)
Asset Owner /Meter Assurance (Meter) |  |  |  | Asset Owner /Meter Assurance (Meter) | Asset Owner /Meter Assurance (Meter)
GEM EVIDENCE (Data Error): | BS EVIDENCE: | MA EVIDENCE: | MA / BS EVIDENCE: | GEM EVIDENCE (Data Error): | GEM EVIDENCE (Data Error):
Figures from source (Asset Owner) | Figures from source (TSO) | Calculation methodology & Raw Data (DN/3rd Party expert) | Figures from source (Shipper) | Figures from source (Asset Owner) | Figures from source (Asset Owner)
NG Validation of the Site Figs (SCADA/Daily Process Sheet) | NG Validation of the TSO Figs (Gemini EU Noms Screens) | NG Validation of the Site Figs (Calculations) | NG Validation of the Shipper Trades (Gemini Screens) | NG Validation of the Site Figs (SCADA/Daily Process Sheet) | NG Validation of the Site Figs (SCADA/Daily Process Sheet)
Shipper Allocations from source (If Alloc only Error) | Reason for error (Input/System/Late submission) | ME/2 AF & AL evidence or Calibration Certs (DN) | All email correspondence | Shipper Allocations from source (If Alloc only Error) | Shipper Allocations from source (If Alloc only Error)
Reason for error (Input/System/Late submission) | All email correspondence | MER (Joint Office/DN) | Shipper approval of new values (if applicable) | Reason for error (Input/System/Late submission) | Reason for error (Input/System/Late submission)
All email correspondence | Shipper approval of new values (if applicable) | All email correspondence |  | All email correspondence | All email correspondence
Shipper approval of new values (if applicable) |  |  |  | Shipper approval of new values (if applicable) | Shipper approval of new values (if applicable)
EVIDENCE (Meter Error): |  |  |  | EVIDENCE (Meter Error): | EVIDENCE (Meter Error):
Calculation methodology & Raw Data (Site/3rd Party expert) |  |  |  | Calculation methodology & Raw Data (Site/3rd Party expert) | Calculation methodology & Raw Data (Site/3rd Party expert)
NG Validation of the Site Figs (Calculations) |  |  |  | NG Validation of the Site Figs (Calculations) | NG Validation of the Site Figs (Calculations)
ME/2 AF & AL evidence or Calibration Certs (Asset Owner) |  |  |  | ME/2 AF & AL evidence or Calibration Certs (Asset Owner) | ME/2 AF & AL evidence or Calibration Certs (Asset Owner)
Supporting Evidence
Additional Information for Meter Error
Responsible
The Shipper or Asset Owner will need to provide the highlighted information

## Slide 18: Appendix 2
Financial incentives to balance

## Slide 19: Financial incentive to balance
The Energy Balancing regime involves maintaining the balance between system inputs and system outputs. National Gas Transmission is responsible for the safety and security of the system - ensuring the physical balance and acting as the residual balancer – trading only when required to maintain this balance.
Shippers using the NTS have a financial responsibility to balance the system, with incentive charges to help them accomplish this.
Under normal circumstances, National Gas can only trade on the On-the-day Commodity Market (OCM), and the System Average Price (SAP) is formulated based on this market (see UNC TPD Section F1.2 System Prices). National Gas do not make or lose money through acting as the residual balancer, or settling shippers’ imbalances. The ‘balancing neutrality’ mechanism ensures money feeds into the ‘neutrality pot’ and is redistributed back to shippers based on their usage of the system.
More detailed information is available in the End to End Balancing Guide.

## Slide 20: Imbalance Charges (Cashout)
Outputs
Output allocations (e.g. supply points, storage injection) and Sell Trades
Imbalance charges encourage shippers to balance their inputs and outputs. This reduces the need for residual balancing actions and helps ensure stable flows on the NTS.
Charges are calculated based on the difference between actual inputs and outputs, with any over or under delivered gas deemed to have been purchased or sold by National Gas for use in the system. The financial incentive works by using System Marginal Prices as the unit price for gas deemed to have been purchased or sold. These are less favourable than SAP, therefore, the shipper pays or receives a less favourable rate than they would have achieved for trading gas themselves on the gas day.
Inputs
Includes entry allocations (e.g. terminals, storage withdrawal) and Buy Trades
Shipper over delivers (position is ‘long’)
i.e. put more into the system than they take out. They are paid for the excess gas but at less than the average price of gas for the day. This is the System Marginal Sell Price (SMPs)
Shipper under delivers (position is ‘short’)
i.e. put less into the system than they take out. They are charged for the difference at greater than the average price of gas for the day. This is the System Marginal Buy Price (SMPb)
Please refer to UNC TPD Section E5.1 Imbalance and Section F2 Daily Imbalances for full details.

## Slide 21: Imbalance Charges (Scheduling)
Scheduling charges encourage shippers to forecast accurately via their nominations. This ensures National Gas can base balancing decisions on the best available information and helps ensure stable flows on the NTS.
Scheduling charges are based on comparing nominations (what shippers tell National Gas they will flow) with allocations (the actual quantity flowed). Note that charges are based on nominations which are in scheduled status within Gemini. Input (Entry) and Output (Exit) Scheduling are calculated independently and have different tolerances applied.
For details please refer to UNC TPD Section F3 Scheduling Charges
Input Scheduling Quantity = Input Nominations - Input Allocations
Note that nominations and allocations at Sub Terminal level are aggregated up to Terminal level.
Tolerances are applied to the nominations when charges are calculated.
Output Scheduling Quantity = Output Nominations - Output Allocations
The tolerances applied vary based upon the Supply Point. Charges will be calculated for any Output Scheduling Quantity in excess of the tolerance and are determined as the quantity multiplied by 1% of the System Average Price for the Gas Flow Day.
Nomination Tolerance | Quantity | Scheduling Charge
First 3% of nomination | Dead band | No charge
3-5% | First Chargeable Input Scheduling Quantity | Quantity multiplied 2% of the SAP
5% + | Second Chargeable Input Scheduling Quantity | Quantity multiplied 5% of the SAP
Supply Point / Group | Tolerance
DMC | 25%
VLDMC or CSEP | 3%
Firm Supply Point Group | 20%
Interruptible Supply Point Group | 25%

## Slide 22: Thank you